The BEMC Preshower
Overview
Investigation with 2007 data
Current status
Where Next
Rory Clarke
Texas A & M University

---
Barrel Electromagnetic Calorimeter layout
The BEMC surrounds the barrel of the TPC. It consists of a number of calorimeter units connected together in sections of 40. These modules cover the barrel in two sections of 60, the West and East sides.
There are 120 modules in all. There are 40 units per module giving 4800 towers in total.
Example of top and side view
of East side module

---
Barrel Electromagnetic Preshower
The Calorimeter units, are made of a sandwich of lead and scintillator
After the first 5 layers it also has a layer for the Shower Max. Detector to improve resolution.
The first two layers are read out for the preshower
Each layer is approx. one radiation length
80% of the electrons are expected to shower over the preshower layer. Hadrons will shower over the length of the tower, allowing these interactions to be separated
The Barrel Preshower is being commissioned
Calorimeter unit, preshower is first two layers

---
2007 Preshower Data
Condition of the ADC readout
One problem with previous years data was the condition of the raw ADC values being
seen. We can see the quality of the 2007 is good.
Mapping issues from 2006 were used in software to improve the 2007 channel mapping
This issue is likely to improve further as the power units are updated and various other issues which have come to light, such as mapping are improved.

---
2007 Minimum Bias, no tracking
One Channel ADC spectra
Data from one run is taken and a fit is made with no cuts
This data is used to find the pedestal
Pedestals are made for all channels and can be subtracted from the data with tracking to remove background

---
2007 Minimum Bias, with tracking
One Channel ADC spectra
Track from TPC must pass through tower
Top: Preshower no pedestal cut.
NOTE: Peak is not at pedestal (Blue line)
Middle: Preshower, pedestal cut(3 sigma), with tracking . A fit has been made to possible Hadron signal (MIP peak). This can be cut to leave electron signal
Lower: Tower with 2.5 sigma Pedestal cut. Showing tower MIP peak

---
2007 Upsilon L2 trigger, with tracking
Once an estimate of the MIP peak has been made, it can be subtracted and the electron
should become clear. This can be best seen in the dEdx plots made with the Upsilon data
Black line = No Preshower
Red line = With preshower
Top plot: Estimated MIP cut for tower
MIP cut for Preshower comes from
channel by channel fits
Line is double Gaussian fit
Lower Plot: Tower cut at pedestal
MIP cut for Preshower comes from
channel by channel fits
Line is double Gaussian fit

---
2007 Upsilon L2 trigger, 1GeV Cut on P
Red line = Hadron region dE/dx
Blue line = Electron region dE/dx
Top plot: Hadron/Electron sector fit
Tower has pedestal cut
Preshower no cuts
Lower Plot:
Prehsower added
Integrated yields estimate:
No preshower; Sig=6.7%
With preshower:Sig=11.6%
Preshower, in this estimate 65% increase in resolution

---
2007 Upsilon L2 trigger, 2 GeV cut on P
2 GeV cut on TPC momentum
Top plot: Hadron/Electron sector fit
Tower has pedestal cut
Preshower no cuts
Lower Plot:
Prehsower added
Note in higher momentum region
Blue “electron” region fits are
almost same magnitude
Integrated yields estimate:
No preshower; Sig=2%
With preshower:Sig=5%
Preshower, in this estimate signal 2.5 times larger increase in resolution

---
Contact Notes:
This work is being conducted at the University of Texas A&M Cyclotron Facility
mio@comp.tamu.edu
rclarke@comp.tamu.edu
mcervantes@comp.tamu.edu